## Slide 1
TWO-PORT NETWORK

## Slide 2: ONE PORT NETWORK
One port network is a two terminal electrical network in which, current enters through one terminal and leaves through another terminal. Example: Resistors, inductors and capacitors are the examples of one port network because each one has two terminals. One port network representation is shown in the following figure.
Here, the pair of terminals, 1 & 1’ represents a port. In this case, we are having only one port since it is a one port network.

## Slide 3: TWO PORT NETWORK
It is an electrical network model with one pair of input terminals and one pair of output terminals. It is commonly used to model the voltage and current characteristics of complex electrical networks.

## Slide 4: TWO PORT NETWORK PARAMETERS
There are various parameters needed to analyze a two-port network. The main two port network parameters are as under:
Impedance Parameters.
Admittance Parameters.
Hybrid Parameters.
Inverse Hybrid Parameters.
Transmission Parameters.
Inverse Transmission Parameters.

## Slide 5: Impedance Parameters OR Z-Parameters OR Open Circuit Parameters

## Slide 6: Z-Parameters OR Impedance Parameters
We know 4 Variables in Two Port Network I1 ,I2, V1 and V2
2 Variables are Independent and 2 Variables are Dependent.
I1 is the current at Port 1 and I2 is the current at Port 2
Similarly V1 is the Voltage at Port1 and V2 is the Voltage at Port 2.
(2)

## Slide 7
Convert equation (1) and (2) into matrix form
Impedance Matrix
Voltage Matrix
Current Matrix

## Slide 8
From equation (1) , If I2 is equal to Zero than Z11
V1 divided by I1 , when port 2 is open circuited
It is also called as Input Impedance with the output port open circuited

## Slide 9
Similarly equation (2) , If I2 is equal to Zero than Z21
V2 divided by I1 , when port 2 is open circuited
It is also called as Forward Transfer Impedance with the output is port open circuited

## Slide 10
Similarly equation (1) , If I1 is equal to Zero than Z12
V1 divided by I2 , when port 1 is open circuited
It is also called as Open Circuit Inverse Transfer Impedance
It is also called as Reverse Transfer Impedance with the Input Port is Open Circuited

## Slide 11
Similarly equation (2) , If I1 is equal to Zero than Z22
V2 divided by I2 , when port 1 is open circuited
It is also called as Output Impedance with the Input Port is Open Circuited

## Slide 12: Q: Determine the Z-Parameter for the given circuit below
Take Loop 1, so - to + = + and + to - = -
) = 0
Solution: From Original Equation of Z-Parameters
) = 0
= 0

## Slide 13
Take Loop 2, so - to + = + and + to - = -
) = 0
Original Equation of Z-Parameters
= 0
= 0
= 0

## Slide 14: Admittance Parameters OR Y-Parameters OR Short Circuit Parameters
Simply Changes Voltages into currents, Currents into voltages and Impedances changes into Admittances
Convert into Matrix Form

## Slide 15
Calculate Y11 , so V2 is zero, when voltage is zero means it is Shor Circuited

## Slide 16: Q: Determine the Y-Parameter for the given circuit below

## Slide 18: Hybrid-Parameters or h-Parameters
To generate the h-parameter, simply output side variables of current with voltage and voltage with currents only I2 = V2 , V2 = I2 and Z = h
Convert into Matrix Form

## Slide 20
Q: Determine the h-Parameter for the given circuit below

## Slide 21
Put the value of I2

## Slide 22: Inverse Hybrid or g-Parameters
To generate the inverse h-parameter, simply input side variables of current with voltage and voltage with currents only V1 = I1 and Z = g
Convert into Matrix Form

## Slide 24
Circuit change into s-domain

## Slide 25

Branch-1

## Slide 26

Branch-2
Put the Value of I1 in eq (B)


## Slide 28: Transmission Parameters OR ABCD Parameters
Primary Current Replaced I1 = Secondary Voltage V2 and V2 = I1 other variables are same.
Convert into Matrix Form
Notice that in computing the transmission parameters, is used rather than the current is considered to be leaving the network, as shown in Fig. 19.31, as opposed to entering the network as in Fig. 19.1(b). This is done merely for conventional reasons; when you cascade two-ports (output to input), it is most logical to think of as leaving the two-port. It is also customary in the power industry to consider as leaving the two-port.

## Slide 29: Transmission Parameters OR ABCD Parameters
The transmission parameters equations provide a measure of how a circuit transmits voltage and current from a source to a load.
They are useful in the analysis of transmission lines (such as cable and fiber) because they express sending-end variables (V1 and I1 ) in terms of the receiving-end variables (V2 and –I2 ).
For this reason, they are called transmission parameters. They are also known as ABCD parameters. They are used in the design of telephone systems, microwave networks, and radars.

## Slide 30: Transmission Parameters OR ABCD Parameters
A and D are dimensionless, B is in ohms, and C is in siemens. Since the transmission parameters provide a direct relationship between input and output variables, they are very useful in cascaded networks.

## Slide 31: Inverse Transmission Parameters OR abcd Parameters
V1 = V2 ,
I1 = V1 ,
I2 = I1
V2 = I2
Convert into Matrix Form
Notice that in computing the transmission parameters, is used rather than the current is considered to be leaving the network, as shown in Fig. 19.31, as opposed to entering the network as in Fig. 19.1(b). This is done merely for conventional reasons; when you cascade two-ports (output to input), it is most logical to think of as leaving the two-port. It is also customary in the power industry to consider as leaving the two-port.

## Slide 32: Inverse Transmission Parameters OR abcd Parameters